## Slide 1: AutoCAD 2D_I
Module 5: Orthographic Projection

## Slide 2: Module Objectives
identify surfaces in two-dimensional views from a given three-dimensional views.
Demonstrate an understanding of the glass box method.
Correctly sketch two-dimensional views from a given three-dimensional view.
Differentiate between first and third angle projection in standard terms.
Produce detailed drawings in either first or third angle projection from a given isometric or oblique drawing.

## Slide 3: Introduction

## Slide 4: Introduction
An orthographic projection is a 2 dimensional representation of a 3 dimensional object. It is a system of drawing views of an object using perpendicular projectors from the object to a plane of projection as shown below.

## Slide 5
Orthographic drawing" refers to a 2-D representation of an object in a view that shows only one side at a time.
Most orthographic drawings occur in multi-drawing sets in order to depict each side, top and bottom view.
Professions in design and construction use these types of drawings to inform the viewer of layout, size and shape.
House floor plans illustrate a common type of orthographic drawing

## Slide 7: Principle views

## Slide 8
There are six principal views in a multiview orthographic projection.
These are the front, back, top, bottom, and left- and right-side views. Of these views or planes, three are referred to as primary planes of projection (vertical, horizontal, and profile).
Most objects are adequately represented by the three primary planes.

## Slide 9: Principle views
Any object can be viewed from six perpendicular views as shown in the figure below

## Slide 10: Principle views
It is clear that there are two main planes used in orthographic projection, one is the horizontal plan and the other is the vertical plan. These planes intersect and divide space into four quadrants. See the figure below

## Slide 11: The glass box method

## Slide 12: Glass Box Approach
Place the object in a glass box
Freeze the view from each direction (each of the six sides of the box) and unfold the box

## Slide 13: The glass box procedure

## Slide 14: The glass box procedure
  The object is placed in a glass box.
  The image of the object is projected on the sides of the box.
  The box is unfolded as shown in Fig
  The sides of the box are the principle views.

## Slide 22: First and Third Angle Projection

## Slide 23: First and Third Angle Projection
As explained in the glass box method mentioned above, when the box is unfolded six views will eventually appear. There are 3 completely different views out of the 5 views and the other 3 are repeated from different angle of projection, this will take us to the two main forms of angle projection.

## Slide 24: First and Third Angle Projection
The first-angle and third-angle projection. In the third-angle each view is placed at the same direction relative to the front view, while in first-angle the places are reversed
Fig 5.6 shows the symbols of the first and third angle projection. An example of the first and third angle projections are shown in Fig. 5.7 and 5.8.

## Slide 25: First and Third Angle Projection
The next figure shows the symbols of the first and third angle projection.

## Slide 26: First and Third Angle Projection
An example of the first and third angle projections are shown in the following figures.

## Slide 28
First and Third Angle Projection

## Slide 29: Activities

## Slide 30: Activities
Class Activity 1
Class Activity 4
Class Activity 2
Class Activity 3
Next

## Slide 31
Next

## Slide 32
Back

## Slide 33
Next

## Slide 34
Back

## Slide 35
The drawing show pictorial and orthographic views of the same block. Complete the table on the right by matching the letters on the pictorial view with the numbers on the orthographic views.
Back

## Slide 36
Draw the Top view of the isometric drawing shown below:
Back

## Slide 37: Homework

## Slide 38
Using the third angle projection, draw the following orthographic views of the isometric drawing shown below.
Front view.
Side view.
Top view.
Back

## Slide 39: The End